## Slide 1: Power Management Solutions for ULP SoCs Deliberate Practice – Session 3
Seyi and Aatmesh
15th May 2013

## Slide 2
Session 2 Review
Problems with Power Management in ULP SoCs
  Efficient voltage regulation required at low voltages
  Multiple regulated output voltages needed
  Energy harvesting is needed to further extend lifetimes
Y. Zhang, et al, "A Batteryless 19uW…. ", JSSC, Jan. 2013.
19µW out of 50µW from TEG
Notes: This work focusses on the infrastructure circuits for the SoC. It needs efficient energy harvesting to increase the amount of harvested energy. Multiple regulated output voltages with higher efficiency to minimize loss and ultra-low power clocking to increase the lifetime in the idle mode.

## Slide 3
Session 2 Review
LDO
I
I
  Input power to the IC
    VDD*I
  Power taken from the source
    Vin*I
  Ideal Efficiency is given by,
    VDD*I/Vin*I=VDD/Vin
  Ex, Vin=1.2V and VDD=0.5V
  Efficiency is 0.41 or ~40%.
  Almost 60% of power is lost in regulation

## Slide 4
Session 2 Review
Research Questions
What alternatives to an LDO can we implement to raise the intrinsic efficiency of the regulator?
How will these alternatives address other problems?
  Multiple outputs
  Overhead (area, power, etc.)
How will energy/performance be monitored?
  e.g. DPM (Shakhsheer et. al.)
How can we harvest energy with higher efficiency?
  State of the Art: 38%
Notes: Optimal energy point exists for each block in the SoC. Sometimes a different operating condition may be selected keeping in mind the performance, sensitivity etc. for the various blocks of the SoC. This drives the need for multiple regulated output voltages for the SoC.

## Slide 5
Proposed Solution – Modified DC-DC Converter
Title: A 400nW Single-Inductor Dual-Input-Tri-Output DC-
DC Buck-Boost Converter with Maximum Power
Point Tracking for Indoor Photovoltaic Energy
Harvesting
Authors: K. Chew, Z. Sun, H. Tang, L. Siek
Notes: Optimal energy point exists for each block in the SoC. Sometimes a different operating condition may be selected keeping in mind the performance, sensitivity etc. for the various blocks of the SoC. This drives the need for multiple regulated output voltages for the SoC.

## Slide 6
DC-DC Converter Review: Buck
Vi
Vo
LOAD
Inductor
Current
Iavg=IL
IL
Iavg=IL
Vx

## Slide 7
Boost Converter
Inductor
Current
Iavg=IL
Iavg=IL

## Slide 8
Proposed Solution – Modified DC-DC Converter
Dual-Input Tri-Output
  Allows three rails and two energy harvesting options
Notes: Optimal energy point exists for each block in the SoC. Sometimes a different operating condition may be selected keeping in mind the performance, sensitivity etc. for the various blocks of the SoC. This drives the need for multiple regulated output voltages for the SoC.

## Slide 9
Proposed Solution – Modified DC-DC Converter
Both Buck and Boost Conversion with single inductor
Buck
Boost
Notes: Optimal energy point exists for each block in the SoC. Sometimes a different operating condition may be selected keeping in mind the performance, sensitivity etc. for the various blocks of the SoC. This drives the need for multiple regulated output voltages for the SoC.

## Slide 10
Example – Boost Converter
10
Inductor
Current
Iavg=IL
Iavg=IL
Notes: Optimal energy point exists for each block in the SoC. Sometimes a different operating condition may be selected keeping in mind the performance, sensitivity etc. for the various blocks of the SoC. This drives the need for multiple regulated output voltages for the SoC.

## Slide 11
Proposed Solution – Modified DC-DC Converter
Title: A 400nW Single-Inductor Dual-Input-Tri-Output DC-
DC Buck-Boost Converter with Maximum Power
Point Tracking for Indoor Photovoltaic Energy
Harvesting
Authors: K. Chew, Z. Sun, H. Tang, L. Siek
Notes: Optimal energy point exists for each block in the SoC. Sometimes a different operating condition may be selected keeping in mind the performance, sensitivity etc. for the various blocks of the SoC. This drives the need for multiple regulated output voltages for the SoC.

## Slide 12
Energy Harvesting for using Solar Cell
Maximum Power Point (MPP) exists
Notes: Ultra Low Power Systems such as body sensor nodes promise to change the way we live. These systems provide rich information about activity, well being and environment. In this illustration BSNs are used to gather vitals of a subject continuously. It can alert a remotely located doctor in case of medical emergency. These systems are small in size and are often remotely located therefore need to have longer lifetime. Changing their batteries often is not possible, so they need to operate from harvested energy. Energy autonomy is central to their wide spread deployment

## Slide 13
MPP is a dynamic quantity
MPP varies with insolation level, temperature etc.
MPP tracking needs to be done we need to operate at MPP
Notes: Ultra Low Power Systems such as body sensor nodes promise to change the way we live. These systems provide rich information about activity, well being and environment. In this illustration BSNs are used to gather vitals of a subject continuously. It can alert a remotely located doctor in case of medical emergency. These systems are small in size and are often remotely located therefore need to have longer lifetime. Changing their batteries often is not possible, so they need to operate from harvested energy. Energy autonomy is central to their wide spread deployment

## Slide 14: Maximum Power Point Tracking
How can this be done?
14
Inductor
Current
Iavg=Im
Iavg=Im

## Slide 15: MPPT Implementation Block Diagram

## Slide 16: Perturb and Observe (P&O)
Paper uses perturb and observe method

## Slide 17: Algorithm for P&O Technique
J.J. Nedumgatt, K.B. Jayakrishnan, S. Umashankar., D. Vijayakumar, and D.P. Kothari, “Perturb and Observe MPPT Algorithm for Solar PV Systems-Modeling and Simulation.” India Conference (INDICON), 2011 Annual IEEE, Dec. 2011 pp.1,6, 16-18.

## Slide 18: Results
Discussed Work [1]

## Slide 19: References
Chew, K.W.R.; Zhuochao Sun; Tang, H.; Siek, L., "A 400nW single-inductor dual-input-tri-output DC-DC buck-boost converter with maximum power point tracking for indoor photovoltaic energy harvesting," Solid-State Circuits Conference Digest of Technical Papers (ISSCC), 2013 IEEE International , vol., no., pp.68,69, 17-21 Feb. 2013
Y. Qiu, C. Van Liempd, B. Op het Veld, P.G. Blanken, and C. Van Hoof, “5μWto-10mW Input Power Range Inductive Boost Converter for Indoor Photovoltaic Energy Harvesting with Integrated Maximum Power Point Tracking Algorithm,” ISSCC Dig. Tech. Papers, pp. 118-119, Feb. 2011.
I. Doms, P. Merken, R. Mertens, and C. Van Hoof, “Integrated Capacitive Power-Management Circuit for Thermal Harvesters with Output Power 10 to 1000μW,” ISSCC Dig. Tech. Papers, pp. 300-301, Feb. 2009.
Y.K. Tan and S.K. Panda, “Energy Harvesting from Hybrid Indoor Ambient Light and Thermal Energy Sources for Enhanced Performance of Wireless Sensor Nodes,” IEEE Trans. Industrial Electronics, vol. 58, no. 9, pp. 4424-4435, Sep. 2011.